ALMA Front-end Optics

M.Carter, A.Baryshev, M.Harman, B.Lazareff. S.Navarro, D.John,G.Ediss C-Y.Tham, F.Tercero. R.Nesti, Y.Sekimoto, M.Matsunaga, H.Ogawa

2004

ALMA Band 9 mirror system

Table of Contents

1:Introduction	4

The Receiver arrangement	4

Optical alignment budget	9

Study	9

Mechanical	10

Thermal	13

Band 1:	23

Optics calculations	25

Optics measurements	25

Band 2:	25

Optics calculations	28

Optics measurements	28

Bands 3 and 4	29

Band 3	30

Optics Calculations	36

Measurements	36

Band 4	36

Optics calculation	38

Band 5	38

Optics calculations	40

Optics measurements	40

Band 6	40

Optics Calculation	45

Optics Measurements	45

Band 7	47

Optics Calculations	51

Optics Measurements	51

Band 8	55

Cryostat Modifications:	58

Optics calculations	58

Optics Measurements	58

Band 9	58

ALMA band 9 optical layout	60

Abstract/Introduction	60

Design concept	60

Equivalent diagonal horn	61

Frequency independent coupling between horn and telescope beam	62

Proposed layout	64

Signal path details	66

LO path details	68

Mirror alignment tolerances	69

Optics design verification	72

7.5	Laser beam propogation	75

7.6	RF beam pattern measurement and analysis	76

Conclusions	83

Band 10	84

Optics calculations	85

Optics measurements	85

Receiver Focus	85

Windows	86

Filters	90

The Optics Calculations	92

The Optics measurements	93

Common Optics	93

Quarterwave Plate	95

Amplitude Calibrator	96

Solar Filter	96

Receiver Alignment	96

Conclusion	97

# 1:Introduction

The Atacama Large Millimeter Array, ALMA, is an international project, whose goal is the construction of a millimeter/ sub millimeter interferometer in the Atacama Desert in Chile.  This array will consist of 64 twelve-meter diameter Cassegrain telescopes operating in the frequency range between 30GHz and 1THz.  This range is divided into 10 frequency bands.  Each telescope will incorporate10 dual polarization receivers giving riser to ten frequency bands within 30GHz to 1THz frequency range.  Each cooled receiver is of module cartridge construction designed in such a way as to fit into a single closed cycle cryostat.

This report describes the optics part of the ALMA receiver cryostat for each frequency band.  This will be coupled with the physical optics calculations that have been carried for the majority of the bands.  Measurements of the prototype optics for first 4 bands 3,6 7 and 9 will be given.   A description of the tolerances for each frequency band is given with respect to the mechanical precision required.  The windows and the infrared filters are described with the measured and calculated performances.  Finally a description of the widget space is given.

This report is also the continuation of the first optics ALMA report, which was published as ALMA Memo 362 Ref 1.

# The Receiver arrangement

The receivers, as have already been reported, are built in cartridges, which are fitted into the base of the cryostat.  A.Orlowska et al have reported the design of the cryostat and cartridges in the ALMA Project Book chapter 5. The design of the cryostat and window and cartridge displacement can be seen in, RAL drawing FEND-40.00.00.00.00-16, by M.Harman Appendix A.  The window and cartridge positions are summarised in table 1 below and can be seen in figure 1 and 2.  From these 2 drawings the coordinates for cryostat and the optics can be seen.  The position 0,0,0 is at the machined surface at the centre of the top plate of the cryostat.

Figure 1: Cryostat cross section

Figure 2: ALMA cryostat top

|  |  |  |  | ALMA cryostat: windows and filters dimensions |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Band | Freq. (GHz) | Wavelength. (mm) | Cartridge Dia. (mm) | Cartridge Radial Loc. (mm) | Beam Radial Loc (mm) | Difference between centres | Window X offset | Window Y offset | 300K hole diameter | 90K hole diameter | 12K hole diameter |
| 1 | 31.3-45 | 7.89 | 170 | 295 | 255 | 40 | -180.3 | 180.3 | 110 | 60 | 60 |
| 2 | 67-90 | 3.85 | 170 | 295 | 255 | 40 | -180.3 | -180.3 | 92 | 50 | 50 |
| 3 | 84-116 | 3.00 | 140 | 335 | 181 | 154 | 54 | -306 | 70 | 95 | 65 |
| 4 | 125-163 | 2.08 | 140 | 335 | 181 | 154 | 54 | 306 | 66 | 74 | 44 |
| 5 | 163-211 | 1.60 | 170 | 295 | 245 | 50 | 173.2 | -173.2 | 66 | 70 | 75 |
| 6 | 211-275 | 1.23 | 170 | 295 | 245 | 50 | 173.2 | 173.2 | 50 | 60 | 65 |
| 7 | 275-370 | 0.93 | 170 | 150 | 100 | 50 | 100 | 0 | 40 | 45 | 50 |
| 8 | 385-500 | 0.68 | 170 | 150 | 100 | 50 | 0 | -103.3 | 35 | 35 | 40 |
| 9 | 602-720 | 0.45 | 170 | 150 | 100 | 50 | 0 | 100 | 20 | 25 | 30 |
| 10 | 787-950 | 0.35 | 170 | 150 | 100 | 50 | -100 | 0 | 20 | 25 | 30 |

Table 1: Optics and cartridge geometry

Table 1 gives the physical coordinates of each cartridge and output window with respect to the Cartridge.  The receiver consists of a cartridge, which is fixed to the bottom of the cryostat.  There are three different constructions of the cartridge, which are as follows:

- Bands 1 and 2:The diameter is 170mm and a cartridge length is 200mm to the 15K plate. This will give a volume of 290mm length by 170mm below the 15K shield to make the optics and receivers.

- Bands 3 and 4:The diameter is 140mm and the cartridge length is 280mm.  This give a volume of 140mm diameter and 210 mm length below the 15K shield.  This was found to be insufficient so that the horn extends past the 15K shield.

- Bands 5-10: The diameter is 170mm with a length of 280mm.  This gives a volume of 170mm diameter and 210mm in length for the optics and the receiver.

The polarization of the receivers will have 2 orthogonal polarizations, but the E-vector of one of these polarizations, A, will point to the centre of the cryostat.

The different frequency bands due to the large variation in wavelength have a large diversity of designs.

The optics of the each band can be summarised into 5 different styles, which are as follows and will be described later in this report:

- Bands 1 and 2 are cooled horns with an ambient lens. The polarisation and local oscillator, LO, injection is done by waveguide couplers and orthomode transducers, OMT.

- Bands 3 and 4 are as 1, but with cooled horns and an ambient offset mirror combination.

- Bands 5 and 6 are cooled horn with cooled twinned elliptical mirrors, but with the LO and polarisation as before.

- Band 7 is as band 6, but the polarisation diplexing is done quasi-optically with a grid.

- Bands 8 –10 have cooled mirrors but both the LO injection and the polarisation diplexing is done quasi-optically with mirrors.

The top plate of the cryostat with its ambient temperature optics is shown in figure 3.  As it can be seen on the right hand side we have the 2 low band frequencies that will be furthest away from the refrigerator.  These are the 2 lensed systems.  In the center we have the 4 high frequency windows for bands 7 –10.  Above and below we have the windows mirror systems for bands 3 and 4.  The windows for bands 5 and 6 are hidden behind the mirror systems.

Figure 3: ALMA cryostat front plate assembly

The optics package not only deals with the optics of each frequency band, but also the optics above the cryostat in the area known as the ‘Widget Space’.  This area is a cylinder of about 1200mm in diameter and 600mm high.  In this space the optics for the water vapour radiometer, WVR, the quarter wave plate for band 7, the solar filter and the amplitude calibration system have to be mounted.  Figure 4 shows the possible set up for the calibration unit and WVR.

Figure 4: Cryostat with common optics

# Optical alignment budget

To ensure that the ALMA front end meets the demanding alignment requirements of ALMA it is necessary that a study be made of the various factors that may influence the alignment of the optical chain.

The purpose of this study is to provide an alignment budget for the different groups who will be supplying components within the optical chain so that this alignment criterion may be met. This budget will then be apportioned to the specific interface control documents (ICD). The provider of these optical components will be expected to adhere to the relevant ICD.

## Study

A prerequisite in understanding this document is a basic knowledge of the components in the optical chain in each band.

As a point of common reference a common co-ordinate system should be utilised to avoid confusion. It is recommended that a similar coordinate system be adopted that is common with the Antenna. For further details about this co-ordinate system please refer to the European or North American antenna ICD titled ‘Basic Antenna definitions’. The illustration below has been extracted from this document for reference, figure 5.

Figure 5: Telescope coordinates

The main elements that affect alignment are as follows

- Mechanical

- Thermal

- Manufacturing

We shall address these items separately for evaluation

### Mechanical

Deformations due to the gravity vector will be induced into the optical chain when antenna is rotated the over the full range of azimuth and elevation. The peak loading condition occurs when a plane normal to the horizon shall be parallel to the optical axis, figure 6.

Figure 6: Cartridge gravity deformation, the scale is in millimeters

The evacuation of the vacuum vessel of the cryostat will cause considerable deformations of the optical mounting surfaces. This has been recognised by the Cryogenics group whom have undertaken a finite element study of the vacuum vessel. As a result of this study various structural members, who provide re-enforcement of the vacuum case, have been added.

The predicted loads on the vacuum case are shown below, figures 7 and 8.

Figure 7: View of vacuum vessel top plate, the scale is in meters

Figure 8: View of vacuum vessel base plate, the scale is in meters

These vacuum deformations will mainly cause an angular error on those bands with ambient temperature optics, i.e. bands 1-4.  Bands 1 and 2 have lenses as there refocusing element and therefore an angular error is not a major problem.  However bands 3 and 4 have mirrors as the refocusing element and the problems of angular deformation will have a large in pact on the beam alignment.  The correction of this misalignment of this misalignment will be done at the integration centres.  This is discussed later in the section on bands 3 and 4.

### Thermal

Thermal contraction will affect the alignment of the optical chain.

Components that have been identified where thermal affects may affect alignment are within the cryostat since this is the area with the largest temperature gradient following alignment and during operation.

Since all components within the cold optical chain are mounted on the cartridge this is the area which requires evaluation.

The internal configuration of the front-end cryostat which utilises individual thermal clamping mechanism on each heat lift stage allows the decoupling of the cartridge structure from the cryostat in the X & Y directions.  The design of the thermal clamps will accommodate approximately 1.5 - 2mm of axial misalignment (in the X & Y directions) on all of the heat lift stages. The Cartridges, which are on the greatest pitch circle radius, are the Band 3 and 4 Cartridges. The Band 3 and 4 Cartridges are on a PCR of 335mm. The thermal links are mounted on copper plate on the 4K stage. The contraction rate of copper from 290K to 4K is approximately 0.04%. From this we can predict that the contraction of the 4K heat stage from the cartridge centre to the cryostat centre will be approximately 1.34mm. Since the Cryostat contracts uniformly about its axis we can conclude that thermal link can accommodate the thermal contraction of the shield and so not affect the alignment of the cartridge pointing.

The thermal contraction along the axis of the cartridge (Z direction) should be evaluated.

There are three different types of cartridges. The cartridges differ in construction in the following manner

Bands 1 & 2 Cartridges are diameter 170 and have 2 Heat lift stages at 90K and 15K

Bands 3 & 4 Cartridges are diameter 140 and have 3 Heat lift stages at 90K, 15K and 4K.

Bands 5 to 10 Cartridges are diameter 170 and have 3 Heat lift stages at 90K, 15K and 4K.

Since we are only interested in the contraction along the axis of the cartridge we need evaluate only the bands 1 & 2 cartridges and band 3 to 10 cartridges separately.

In Figure 9 below we can see the band 6 cartridge.  We can take this as an example of the problems with the tolerancing of the cartridge system, which is explained by the schematic in figure 10.  The cartridge manufacturers must reference their optics to the 4K plate.  However the cryostat reference is the bottom plate and the telescope to cryostat reference is the FESS.  There is a cylinder of 280mm long, made in 3 sections that separate these two references.

Figure 9: ALMA band 6 Cartridge, receiver and Optics

Figure 10: Schematic of the ALMA front end

| Tolerances for optics band 1 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Telescope to FESS (A1) | FESS to cryostat (A1-A2) | 300K cartridge to cryostat (A2-A3) | 300K cartridge to 15K cartridge (A3-A4) | Cartridge (Cold optics internal budget.) (A4-A5) | Cryostat to Warm optics interface (A2-A6) | Warm optics internal budget (A6-A7) |
| Linear | Coefficient | Radians/mm |  |  | 5.30E-03 | 5.30E-03 | 5.30E-03 | 5.30E-03 | 5.30E-03 |
|  | Positional Tolerance | mm |  |  | 0.05 | 0.125 | 0.04 | 0.5 | 0.6 |
|  | Contribution | radian |  |  | 2.65E-04 | 6.63E-04 | 2.12E-04 | 2.65E-03 | 3.18E-03 |
| Angular | Coefficient | rd/rd | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
|  | Angular Tolerance | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 0.00E+00 | 2.22E-04 | 2.97E-04 |
|  | Angular Tolerance | degree | 5.16E-02 | 1.04E-02 | 2.30E-02 | 1.70E-02 | 0.00E+00 | 1.27E-02 | 1.70E-02 |
|  | Contribution | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 0.00E+00 | 2.22E-04 | 2.97E-04 |
|  | Pitch circle radius | mm | N/A | 550.00 | 295.00 | 85.00 |  | 450.00 |  |
|  | Co-planarity (Flatness) | mm | N/A | 0.10 | 0.10 | 0.10 |  | 0.10 |  |
| Cartridge |  |  |  |  |  |  |  |  |  |
| Worst case |  | 2.12E-04 |  | Goal | 4.00E-03 |  |  |  |  |
| RMS |  | 1.50E-04 |  |  |  |  |  |  |  |
| System |  |  |  |  |  |  |  |  |  |
| Worst-Case |  | 9.27E-03 |  | Goal | 6.00E-03 |  |  |  |  |
| RMS |  | 4.35E-03 |  |  |  |  |  |  |  |

Table 2

| Tolerances for optics band 2 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Telescope to FESS (A1) | FESS to cryostat (A1-A2) | 300K cartridge to cryostat (A2-A3) | 300K cartridge to 15K cartridge (A3-A4) | Cartridge (Cold optics internal budget.) (A4-A5) | Cryostat to Warm optics interface (A2-A6) | Warm optics internal budget (A6-A7) |
| Linear | Coeff | rd/mm |  |  | 0.011 | 0.011 | 0.022 | 0.011 |  |
|  | Positional Tolerance | mm |  | 0.2 | 0.05 | 0.05 | 0.04 | 0.5 |  |
|  | Contribution | radian |  |  | 5.50E-04 | 5.50E-04 | 8.80E-04 | 5.50E-03 |  |
| Angular | Coeff | rd/rd | 1 | 1 | 1 | 1 | 1 | 1 | 1 |
|  | Angular Tolerance | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 0.00E+00 | 2.22E-04 | 2.97E-04 |
|  | Angular Tolerance | degree | 5.16E-02 | 1.04E-02 | 2.30E-02 | 1.70E-02 | 0.00E+00 | 1.27E-02 | 1.70E-02 |
|  | Contribution | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 0.00E+00 | 2.22E-04 | 2.97E-04 |
|  | Pitch circle radius | mm | N/A | 550.00 | 295.00 | 85.00 |  | 450.00 |  |
|  | Co-planarity (Flatness) | mm | N/A | 0.10 | 0.10 | 0.10 |  | 0.10 |  |
| Cartridge |  |  |  |  |  |  |  |  |  |
| Worst case |  | 4.40E-04 |  | Goal | 4.00E-03 |  |  |  |  |
| RMS |  | 3.11E-04 |  |  |  |  |  |  |  |
| System |  |  |  |  |  |  |  |  |  |
| Worst-Case |  | 9.78E-03 |  | Goal | 6.00E-03 |  |  |  |  |
| RMS |  | 5.73E-03 |  |  |  |  |  |  |  |

TABLE 3

| Tolerances for optics band 3 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Telescope to FESS (A1) | FESS to cryostat (A1-A2) | 300K cartridge to cryostat (A2-A3) | 300K cartridge to 4K cartridge (A3-A4) | Cartridge (Cold optics internal budget.) (A4-A5) | Cryostat to Warm optics interface (A2-A6) | Warm optics internal budget (A6-A7) |
| Linear | Coefficient | Rd/mm |  |  | 0.0067 | 0.0067 | 0.0134 | 0.0067 | 6.70E-03 |
|  | Positional Tolerance | mm |  | 0.2 | 0.05 | 0.1 | 0.06 | 0.05 | 0.05 |
|  | Contribution | radian |  |  | 3.35E-04 | 6.70E-04 | 8.04E-04 | 3.35E-04 | 3.35E-04 |
| Angular | Coefficient | rd/rd | 1 | 1 | 2 | 1 | 0.048 | 2 | 2 |
|  | Angular Tolerance | radian | 9.00E-04 | 1.82E-04 | 8.74E-04 | 2.97E-04 | 5.93E-04 | 2.22E-04 | 1.75E-03 |
|  | Angular Tolerance | degree | 5.16E-02 | 1.04E-02 | 5.00E-02 | 1.70E-02 | 3.40E-02 | 1.27E-02 | 1.00E-01 |
|  | Contribution | radian | 9.00E-04 | 1.82E-04 | 1.75E-03 | 2.97E-04 | 2.85E-05 | 4.44E-04 | 3.49E-03 |
|  | Pitch circle radius | mm | N/A | 550.00 | 345.00 | 70.00 |  | 450.00 |  |
|  | Co-planarity (Flatness) | mm | N/A | 0.10 | 0.10 | 0.10 |  | 0.10 |  |
| Cartridge |  |  |  |  |  |  |  |  |  |
| Worst case |  | 4.16E-04 |  | Goal | 4.00E-03 |  |  |  |  |
| RMS |  | 3.00E-04 |  |  |  |  |  |  |  |
| System |  |  |  |  |  |  |  |  |  |
| Worst-Case |  | 9.57E-03 |  | Goal | 6.00E-03 |  |  |  |  |
| RMS |  | 4.22E-03 |  |  |  |  |  |  |  |

Table 4

| Tolerances for optics band 4 |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Telescope to FESS (A1) | FESS to cryostat (A1-A2) | 300K cartridge to cryostat (A2-A3) | 300K cartridge to 4K cartridge (A3-A4) | Cartridge (Cold optics internal budget.) (A4-A5) | Cryostat to Warm optics interface (A2-A6) | Warm optics internal budget (A6-A7) |
| Linear | Coefficient | rd/mm |  |  | 0.0067 | 0.0067 | 0 | 0.0067 | 6.70E-03 |
|  | Positional Tolerance | mm |  | 0.2 | 0.05 | 0.1 | 0 | 0.05 | 0.07 |
|  | Contribution | radian |  |  | 3.35E-04 | 6.70E-04 | 0.00E+00 | 3.35E-04 | 4.69E-04 |
| Angular | Coefficient | rd/rd | 1 | 1 | 1 | 1 | 0 | 2 | 4 |
|  | Angular Tolerance | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 0.00E+00 | 2.22E-04 | 2.97E-04 |
|  | Angular Tolerance | degree | 5.16E-02 | 1.04E-02 | 2.30E-02 | 1.70E-02 | 0.00E+00 | 1.27E-02 | 1.70E-02 |
|  | Contribution | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 0.00E+00 | 4.44E-04 | 1.19E-03 |
|  | Pitch circle radius | mm | N/A | 550.00 | 345.00 | 70.00 |  | 450.00 |  |
|  | Co-planarity (Flatness) | mm | N/A | 0.10 | 0.10 | 0.10 |  | 0.10 |  |
| Cartridge |  |  |  |  |  |  |  |  |  |
| Worst case |  | 0.00E+00 |  | Goal | 4.00E-03 |  |  |  |  |
| RMS |  | #VALUE! |  |  |  |  |  |  |  |
| System |  |  |  |  |  |  |  |  |  |
| Worst-Case |  | 4.11E-03 |  | Goal | 6.00E-03 |  |  |  |  |
| RMS |  | 1.90E-03 |  |  |  |  |  |  |  |

TABLE 5

| Tolerances for optics band 6 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Cold optics internal budget break down (A5) |
|  |  |  | Telescope to FESS (A1) | FESS to cryostat (A1-A2) | 300K cartridge to cryostat (A2-A3) | 300K cartridge to 4K cartridge (A3-A4) | Cartridge (Cold optics internal budget.) (A4-A5) | Mirror 2 w/r Optical mount | Upper Assembly w/r to M2 | Mirror 1 w/r to Roof | Horn w/r to Mirr.1 | Optical mount to cartridge |
| Linear | Coefficient | rd/mm |  |  |  |  | 0.087 | 0.013 | 0.013 | 0.038 | 0.023 |  |
|  | Positional Tolerance | mm |  | 0.2 | 0.2 | 0.05 | 0.14 | 0.02 | 0.08 | 0.02 | 0.02 |  |
|  | Contribution | radian |  |  |  |  | 2.52E-03 | 2.60E-04 | 1.04E-03 | 7.60E-04 | 4.60E-04 |  |
| Angular | Coefficient | rd/rd | 1 | 1 | 1 | 1 | 5.11 | 2 | 1.034 | 2.07 | 0.006 | 1 |
|  | Angular Tolerance | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 1.49E-03 | 2.97E-04 | 2.97E-04 | 2.97E-04 | 2.97E-04 | 2.97E-04 |
|  | Angular Tolerance | degree | 5.16E-02 | 1.04E-02 | 2.30E-02 | 1.70E-02 | 8.51E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 |
|  | Contribution | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 1.81E-03 | 5.94E-04 | 3.07E-04 | 6.15E-04 | 1.78E-06 | 2.97E-04 |
|  | Pitch circle radius | mm | N/A | 550.00 | 295.00 | 85.00 |  |  |  |  |  |  |
|  | Co-planarity (Flatness) | mm | N/A | 0.10 | 0.10 | 0.10 |  |  |  |  |  |  |
| Cartridge |  |  |  |  |  |  |  |  |  |  |  |  |
| Worst case |  | 4.33E-03 |  | Goal | 4.00E-03 |  |  |  |  |  |  |  |
| RMS |  | 1.69E-03 |  |  |  |  |  |  |  |  |  |  |
| System |  |  |  |  |  |  |  |  |  |  |  |  |
| Worst-Case |  | 5.79E-03 |  | Goal | 6.00E-03 |  |  |  |  |  |  |  |
| RMS |  | 3.28E-03 |  |  |  |  |  |  |  |  |  |  |

Table 6

| Tolerances for optics band 7 |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Cold optics internal budget break down (A5) |
|  |  |  | Telescope to FESS (A1) | FESS to cryostat (A1-A2) | 300K cartridge to cryostat (A2-A3) | 300K cartridge to 4K cartridge (A3-A4) | Cartridge (Cold optics internal budget.) (A4-A5) | Mirror 2 w/r Baseplate | Upper Assembly w/r to M2 | Grid w/r to roof | Mirror 1 w/r to Roof | Horn w/r to Mirr.1 | Optical mount to cartridge |
| Linear | Coefficient | Rd/mm |  |  |  |  | 0.114 | 0.013 | 0.013 | 0.024 | 0.037 | 0.027 |  |
|  | Positional Tolerance | mm |  | 0.2 | 0.2 | 0.05 | 0.16 | 0.02 | 0.08 | 0.02 | 0.02 | 0.02 |  |
|  | Contribution | radian |  |  |  |  | 3.06E-03 | 2.60E-04 | 1.04E-03 | 4.80E-04 | 7.40E-04 | 5.40E-04 |  |
| Angular | Coefficient | rd/rd | 1 | 1 | 1 | 1 | 5.735 | 2 | 1.034 | 0.625 | 2.07 | 0.006 | 1 |
|  | Angular Tolerance | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 1.78E-03 | 2.97E-04 | 2.97E-04 | 2.97E-04 | 2.97E-04 | 2.97E-04 | 2.97E-04 |
|  | Angular Tolerance | degree | 5.16E-02 | 1.04E-02 | 2.30E-02 | 1.70E-02 | 1.02E-01 | 1.70E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 |
|  | Contribution | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 2.00E-03 | 5.94E-04 | 3.07E-04 | 1.86E-04 | 6.15E-04 | 1.78E-06 | 2.97E-04 |
|  | Pitch circle radius | mm | N/A | 550.00 | 150.00 | 85.00 |  |  |  |  |  |  |  |
|  | Co-planarity (Flatness) | mm | N/A | 0.10 | 0.10 | 0.10 |  |  |  |  |  |  |  |
| Cartridge |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Worst case |  | 5.06E-03 |  | Goal | 4.00E-03 |  |  |  |  |  |  |  |  |
| RMS |  | 1.78E-03 |  |  |  |  |  |  |  |  |  |  |  |
| System |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Worst-Case |  | 6.84E-03 |  | Goal | 6.00E-03 |  |  |  |  |  |  |  |  |
| RMS |  | 3.80E-03 |  |  |  |  |  |  |  |  |  |  |  |

TABLE 7

| Tolerances for optics band 9 |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Cold optics internal budget break down (A5) |
|  |  |  | Telescope to FESS (A1) | FESS to cryostat (A1-A2) | 300K cartridge to cryostat (A2-A3) | 300K cartridge to 4K cartridge (A3-A4) | Cartridge (Cold optics internal budget.) (A4-A5) | Mirror 2 w/r Baseplate | Upper Assembly w/r to M2 | Grid w/r to roof | Mirror 1 w/r to Roof | Horn w/r to Mirr.1 | Baseplate to cartridge |
| Linear | Coefficient | Rd/mm |  |  |  |  | 0.205 | 0.039 | 0.039 | 0.024 | 0.064 | 0.039 |  |
|  | Positional Tolerance | mm |  | 0.2 | 0.2 | 0.05 | 0.16 | 0.02 | 0.08 | 0.02 | 0.02 | 0.02 |  |
|  | Contribution | radian |  |  |  |  | 6.44E-03 | 7.80E-04 | 3.12E-03 | 4.80E-04 | 1.28E-03 | 7.80E-04 |  |
| Angular | Coefficient | Rd/rd | 1 | 1 | 1 | 1 | 9.098 | 2 | 1.034 | 4.43 | 1.63 | 0.004 | 1 |
|  | Angular Tolerance | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 1.78E-03 | 2.97E-04 | 2.97E-04 | 2.97E-04 | 2.97E-04 | 2.97E-04 | 2.97E-04 |
|  | Angular Tolerance | degree | 5.16E-02 | 1.04E-02 | 2.30E-02 | 1.70E-02 | 1.02E-01 | 1.70E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 | 1.70E-02 |
|  | Contribution | radian | 9.00E-04 | 1.82E-04 | 4.02E-04 | 2.97E-04 | 3.00E-03 | 5.94E-04 | 3.07E-04 | 1.32E-03 | 4.84E-04 | 1.19E-06 | 2.97E-04 |
|  | Pitch circle radius | mm | N/A | 550.00 | 150.00 | 85.00 |  |  |  |  |  |  |  |
|  | Co-planarity (Flatness) | mm | N/A | 0.10 | 0.10 | 0.10 |  |  |  |  |  |  |  |
| Cartridge |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Worst case |  | 9.44E-03 |  | Goal | 4.00E-03 |  |  |  |  |  |  |  |  |
| RMS |  | 3.91E-03 |  |  |  |  |  |  |  |  |  |  |  |
| System |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Worst-Case |  | 1.12E-02 |  | Goal | 6.00E-03 |  |  |  |  |  |  |  |  |
| RMS |  | 7.18E-03 |  |  |  |  |  |  |  |  |  |  |  |

Table 8

# Band 1:

Band 1 is a horn lens combination.  The horn is attached to the 15K plate of the cartridge.  The lens acts as the window.  The lens is attached to the support, which is proud of the cryostat top plate.  The beam needs to be inclined inwards towards the center of the cryostat by 2.5°.

Table 9

Band 1 Schematic

Figure 11: Band 1 Optics design

R.Nesti of ARCETRI designed the horn.  This design can be seen below.  He has varied the pitch, heights and widths of the teeth to improve the overall bandwidth of the horn.  The changes and the expected and measured return loss of the horn are given in figures 3 and 4.  The horn with its counterpart for band 2 are shown in figure x.  The horn was machined out of an aluminium block.  The horn and measurements are shown in appendix 1.

Figure 12: Band 1 horn design

Figure 13: Band 1 horn mismatch

Window: The window is the high density polyethylene, HDPE lens with an average thickness of ~ 50mm

Infrared Filter is attached to the 90K shield.  This is solid grooved Teflon with a thickness of 10.9mm.

### Optics calculations

Gaussian beam simulations Appendix E

Physical optics TBD

### Optics measurements

TBD

# Band 2:

R.Nesti of ARCETRI designed the horn.  This is a similar horn lens combination that has already been reported in reference 1.  The horn is attached to the 15K plate of the cartridge.  The lens acts as the window.  The lens is attached to the top of the cryostat.  The beam needs to be inclined inwards towards the center of the cryostat by 2.5°.

Table 10 Band 2 optics parameters

Figure 14: Band 2 Optics Design

The horn was redesigned by R.Nesti of Arcetri.  He has varied the pitch, heights and widths of the teeth to improve the overall bandwidth of the horn.  The changes and the expected and measured return loss of the horn are given in figures 5 and 6.  The horn with its counterpart for band 1 is shown in figure 7.  The horn was machined directly out of an aluminium block.  The horn and measurements are shown in appendix 2.

Figure 15: Band 2 horn design

Figure 16: Band 2 horn mismatch

### Optics calculations

Gaussian beam simulations Appendix E

Physical optics TBD

### Optics measurements

TBD

Figure 17: and 1 and 2 horns

# Bands 3 and 4

Bands 3 and 4 are made on the small 140mm diameter cartridges, and are offset from the cryostat centre by 335mm.  There is not enough room inside the cartridges to have cold optics as for bands 5 and above.  The technique of using ambient temperature lenses, as bands 1 and 2, would have too much loss at these frequencies, and further to this the telescope beam wants to be brought closer to the center of the cryostat.  The system chosen is to have ambient temperature mirrors.  The beam coming from the telescope is incident on a flat mirror, which reflects the beam out to an elliptical mirror and then the beam is focused down into the cryostat onto the horn.  The precise designs of the optics of the 2 designs for these cartridges will be given later. Figure 8 shows the mirror assembly.

.

Figure 18: Mirror Assembly bands 3 with alignment tool

As shown in the section 3 dealing with the alignment budget, it can be seen that these mirrors cannot be aligned accurately enough against the horn by means of machining tolerances alone.  This is mainly due to two reasons:

- Overall alignment tolerances.  The alignment reference for the horn is the 4K plate of the cartridge.  This is then referenced to the rear face of the cryostat.  The cryostat sides to the front plate of the cryostat in turn reference this.  The overall increase in tolerances in this train is found to be too great to arrive within the accepted tolerance budget.

- The deformation of the cryostat front and back plates due to vacuum is too large, to compensate by manufacturing tolerances alone, figure 9.  These deformations are of the order of 0.35mm for each surface.

To overcome these problems, the mirror assembly will have to be aligned to the cryostat at the integration centres.  A mirror alignment tool has been designed and made, figure 10.  At the integration centres the beam pattern will be measured, the alignment tool will adjust the mirror position to have the correct beam profile etc..   The mirror assembly will then be screwed and pinned securely.

.

Figure 19: Band 3 and 4 Optics alignment tool

# Band 3

The design of the band 3 optics was changed from that given in Memo 362.  The former design had the horn protruding above the cryostat top plate.  This made the cryostat manufacture complicated with respect to the filters and windows.  It was decided that a modification to the design change was required.

To improve the design, but to keep the overall optics concept of a horn feeding external mirrors, the waist of the horn had to be increased and moved to the horn mouth.  Two different design were considered:

- A phase corrected lensed horn proposed by J-A.Lopez Fernandez and F.Tercero of Yebes Observatory

- A profiled horn proposed by R.Nesti of Arcetri.

After preliminary studies the lensed horn was accepted.  This horn, figures 20 and 22, is an open horn with an 18º flare half angle.  The horn design is by M.Carter, figure 20.  The horn is machined directly out of an aluminium block.

Built into this horn is a round to square waveguide, which can be machined directly into the aluminium block. A 0.9mm long square section with the corners chamfered is machined into the 3mm diameter circular waveguide.  This transition was designed by A-L. Fontana and can be seen in figure 16.  The theoretical curves for the mismatch for the horn and transition are shown in figure 23 and 24.

The lens is made out of high density polyethylene, HDPE.  The horn shown and measured used a dielectric constant of 2.32.  This number is modified to 2.44 for the use at 4K temperatures.  The reasons for the was given by A.Kerr of NRAO in a private correspondence, base on the work of J.Lamb.  “We realized that there was a change in the refractive index and geometry of the lens when cooled.  The contraction δ (=δL/L) from room temperature to 4K for Teflon and polyethylene is 2.1% and 2.4%, respectively.  The contraction alone (at constant dielectric constant) will shorten the focal length of the lens by the same percentage δ.  The relative increase in density of the lens of the lens (~3δ) causes the refractive index to increase, as one might expect.  According to the Clausius-Mossotti equation, (εr-1)/(εr+2)α density.  The resulting change in focal length on cooling due to both effects f295/f4 = 1.095 (Teflon) and 1.14 (polyethylene).  About 80% is due to the change in the refractive index alone.

F.Tercero and J-A. Lopez Fernandez have done a study to try and improve the mismatch of the horn lens combination from that shown below in figure 24.  As it can be seen the mismatch rises to about –20dB at the bottom of the band.  This study can be seen in annex c.

r

Figure 20: Horn 3b design

Figure 21: Round to square waveguide transition

Figure 22: Band 3 Horn

Figure 23:Theoretical and measured mismatch of the horn

Figure 24 Theoretical mismatch of the horn with lens

The polar diagrams for the horn, with and without the lens were measured.  An example of the measurements are shown below.  The cross polar performance was better than –20dB across the frequency band.

figure 25: Horn bandand lens combination polar diagram2

The schematic of the optics can be seen in Figure 19 below and the parameters are given in table 5.  This is a design by F.Tercero of Yebes Observatory.  As can be seen the horn is now well below the window and both of the 90K and 15K filters can be fitted.

Figure 26: design of the band 3b optics

| Frequency [GHz] |  | 84 | 89 | 100 | 116 |
| --- | --- | --- | --- | --- | --- |
| ( [mm] |  | 3.568958 | 3.368455 | 2.997925 | 2.584418 |
| Horn diameter | 29.800 |  |  |  |  |
| Horn axial length | 45.857 |  |  |  |  |
| Horn slant length | 48.217 |  |  |  |  |
| Horn waist, w0 |  | 4.727 | 4.522 | 4.121 | 3.640 |
| Horn waist offset, (z(w0) |  | -34.711 | -35.658 | -37.386 | -39.249 |
| Waist at horn aperture |  | 9.588 | 9.588 | 9.588 | 9.588 |
| flens | 53.589 |  |  |  |  |
| Waist at lens aperture |  | 10.388 | 10.388 | 10.388 | 10.388 |
| d1 | 209.779 |  |  |  |  |
| Rs1 | 190.745 | 252.795 | 258.068 | 270.743 | 291.812 |
| f1 | 203.000 |  |  |  |  |
| Ri1 | 811.315 | 1030.570 | 951.322 | 811.315 | 667.003 |
| Waist at mirror 1 | (dia. = 130) | 25.183 | 24.015 | 21.892 | 19.593 |
| d2 | 160.025 |  |  |  |  |
| Waist at mirror 2 | (dia. = 115) | 22.464 | 21.215 | 18.908 | 16.338 |
| zw(Cass.) | 287.459 | 233.802 | 230.453 | 224.766 | 219.191 |
| wCass. |  | 22.143 | 20.905 | 18.614 | 16.054 |
| dmirror-subrefl |  | 6281.65 | 6281.65 | 6281.65 | 6281.65 |
| wsubrefl | (dia. = 750) | 318.795 | 318.795 | 318.795 | 318.795 |
| Rsubrefl | 5994.20 | 6078.65 | 6078.65 | 6078.65 | 6078.65 |
| Edge Taper (dB) | 12.00 | 12.62 | 12.62 | 12.62 | 12.62 |
| Multimode Truncation (dB) | 10.00 | 9.93 | 9.93 | 9.93 | 9.93 |

Table 8

### Optics Calculations

Appendix I

### Measurements

TBD

# Band 4

Band 4, as with band 3 has been modified, from the design given in the ALMA Memo 362.  The redesign was for the same reasons as for band 3.  The band 4 optics design was done by K.Kimura and H.Ogawa can be seen in figure 27 and the parameters are given in table 9. the horn design is shown in figure 28.  Their work was in close collaboration with C-Y. Tham with the  physical optics calculations.

Figure 27: Band 4 design

Figure 28: band 4 horn design

Table 9

### Optics calculation

Appendix H

Optics Measurements:

Measurements for this band have not yet been made.

# Band 5

This is a low priority band.  The design has not been changed, since the Lamb report, reference 1.  This design can be seen in figure 21 below and the parameters are given in table 9.  The design essentially is the same, as that will be given for band 6.  There has not been any physical optics calculations made on this band.

Table 10 ALMA band 5 Quasi-optics parameters

Figure 29: Band 5 Schematic

### Optics calculations

Gaussian beam simulations Appendix E

Physical optics TBD

### Optics measurements

TBD

# Band 6

This band is essentially the same as stated in the previous report, which is a single horn being fed by a pair elliptical mirrors.  However after the physical optics study, it was felt that a better performance is attained with slight changes. The optics parameters for this band are given below in table 7 and the optics on the built cartridge is shown in figure 30.

Table 11

Figure 30: Band 6 system design

Figure 31: Band 6 horn

Figure 32: Band 6 horn design

M.Carter designed the horn as shown in figures 31 and 32.  The horn is made by conventional electroforming techniques by Custom Microwave.  The horn mismatch is shown in figure 33, and it is compared to the mismatch of a Custom Microwave Ltd. Standard conical horn.  The mismatch of the horn is better than shown, due to a degradation of the measurements caused by the use of a non standard waveguide being used in the circular to rectangular transition.  However as can be seen the horn will have a better than –20dB return loss over the frequency band.

Figure 33: Band 6 horn mismatch

The return losses of the horns were measured on a vector analyzer to cover the frequency 210 to 275Ghz.  The problems with the measurements were change of standard in the waveguide, which put an increased mismatch in the measurements. As can be seen the measured mismatch is equivalent to that of a WR3 conical horn.  From this the mismatch is probably better than –20dB across the frequency range.

The polar diagram horn was measured across the band was measure across the frequency band of 210-275GHz.  As can be seen in figure 34 for 240Ghz beam is clean and symmetric.

Figure 34 Horn polar diagram at 240GHz

### Optics Calculation

Appendix F

### Optics Measurements

The measurements of the entire optics for band 6 were made over the frequency band.  The resume of these measurements show that the beam waist is approximately at the correct position, with the required inclinations in the 2 planes to point to the center of the secondary.  The waist also has a size which gives a –12dB edge taper on the secondary.

Figure 35:Band 6 optics results

Figure 36 Amplitude (left) and Phase (right) measurements at 240GHZ

# Band 7

Band 7 is the lowest frequency band that does not use an orthomode transducer but a grid as a polarization splitter.  The conventional technique of putting the grid between the 2 horns was not possible.  The grid had to be put between the 2 mirrors, which means that:

- The mirrors M1 and M2 could not compensate each other with respect to cross-polar performance.

- Two M1 mirrors were required to illuminate both horns.

- The reflection angle on mirror 2 was kept small at 25º and the focal length comparatively long to ensure a low cross polar return.

Figure 36: Band 7 optics design

Figure 37: ALMA band 7 optics

Table 12

The horn design is shown below with the horn.  This horn was designed by. M.Carter, and can be seen in figure27 and 28.  To reduce the length of the horn the circular to rectangular waveguide transition was made using a step transition designed by A-L.Fontana.  This also helped in the manufacture of the horns since it was found that the earlier tapered transition tended to bend in the electroforming process.

Figure 38: Band 7 horn design

Figure 39: band 7 horn

Figure 40: Return loss band 7 horn

The return loss of the horn is shown above against the theoretical curve.  These measurements were made on a newly modified vector analyzer.  At the time of the measurement it could not cover the frequencies above 360GHz and the measurements between about 285-305Ghz are falsely high.  The polar diagrams were measured for the horns and an example can be seen in figure 30.  The lobes are symmetric over the whole frequency band, the side lobes are about –25dB below the main beam and the cross polar diagrams are also of the same order.

Figure 41: Co and cross polar band 7 horn measurements at 309GHz

### Optics Calculations

Appendix F

### Optics Measurements

The system measurements were made on the antenna test range across the frequency band.  Two measurements are shown below.  In figure 42 a cross scan giving the co and cross polar measurements can be seen.  The cross polarisation is of the order of –30dB on axis.  In figure 43 a 2D scan at 324GHZ show that the beam is symmetrical in both amplitude and phase with an angle in the direction of the sub-reflector.  The resume of the measurements are given in figure 44.

Figure 42: co and crosspolar system measurement at 276GHz

Figure 43: Band 7 2D scan at 324GHz

Figures 44: A,B,C, and D a resume of the band 7 antenna measurements.

As can be seen in the figures 44 above the inclination angle was correct with in experimental error for both horns and orientation of the measurements.  The sub-reflector edge taper is about –11.5dB.  There seems to be wider than expected variation in waist position at the bottom end of the frequency band.  This should be inspected.

Figure 45: Complete band 7 cartridge

In figure 45 the completed band 7 cartridge is shown.  The 2 horns with the two mirrors above can be seen.  Also the grid separating the 2 polarisations.

# Band 8

Band 8 uses one focusing mirror in stead of the normal two. It is so simple that it is easy to align the mirror and the horn and easy to fabricate the optics block. Optics parameters are given in Table 6.

Table 13 Band 8 optical parameters

The polarization splitter is a wire grid. The signal path is symmetrical for vertical and horizontal polarization. The reflection angle at the focusing mirror is 20 degree.

Optical block was designed mechanically by Naohisa Satou of NAOJ. It is machined from a pure Aluminum block with some anchor points to measure easily with a CNC coordinated measuring machine. The weight of optics block excluding the wire grid and 2SB mixer block is 0.8 kg.

Local oscillator signal is injected to SIS mixers with a waveguide coupler designed by Shinichiro Asayama of NAOJ.

The optics block has an inclination angle of 1.20 degree for the subreflector.

Figure 45:　Band 8 optics block design

The band 8 horn was designed by M. Matsunaga of Ehime University and can be seen in figure 30 below.

Figure 46: Band 8 horn design

Beam pattern of band 8 optics (engineering model) was measured with a vector network analyzer at NAOJ. The engineering model is similar to preproduction model, but difference is that the reflection angle is 22.5 degree.

Figure 47: Beam pattern of Band 8 Engineering Model (EM).

## Cryostat Modifications:

We changed band 8 optics design to accommodate 2SB mixer scheme. We would like to request to change window poison for band 8 to [X 0.0, Y -129.4] with assuming that the center of band 8 cartridge body is [X 0.0, Y -150.0].

### Optics calculations

Appendix H

### Optics Measurements

TBD

# Band 9

Band 9 has undergone a major redesign since the PDR.  There was a problem with the local oscillator scheme in the previous design.  The design chosen is similar to that described for band 7 with the polarization grid between the 2 elliptical mirrors.  The design has to be more complicated than band 7 to allow the injection of the local oscillator into each of the mixers.  This design is undergoing a physical optics study, and the horn has been designed and is being manufactured.

The new design can be seen in a report by A.Baryshev below

This documents describes detailed optical layout of ALMA band 9 cartridge. It mainly contains the data missing in the band 9 optics presentation from ALMA week in Granada. The document “band9_optics.pdf” is essential for complete understanding of band 9 optical layout.

Quasi-optics Gaussian beam parameters.

| Frequency [GHz] |  | 602 | 661 | 720 |
| --- | --- | --- | --- | --- |
| ( [mm] |  | 0.497994 | 0.453544 | 0.416378 |
| Horn diameter | 5.066 |  |  |  |
| Horn axial length | 15.516 |  |  |  |
| Horn slant length | 15.722 |  |  |  |
| Horn waist, w0 |  | 1.115 | 1.059 | 1.006 |
| Horn waist offset, (z(w0) |  | -8.364 | -9.089 | -9.735 |
| Waist at horn aperture, wha |  | 1.630 | 1.630 | 1.630 |
| d1 | 44.484 |  |  |  |
| Rs1 | 54.698 | 54.012 | 54.698 | 55.293 |
| f1 | 24.862 |  |  |  |
| Ri1 | 45.579 | 46.067 | 45.579 | 45.174 |
| Waist at mirror 1, wM1 | (dia. = 45) | 7.595 | 7.381 | 7.214 |
| (1 | 50.0( |  |  |  |
| zw1 |  | 45.340 | 44.924 | 44.584 |
| w1 |  | 0.954 | 0.885 | 0.824 |
| d2 | 95.906 |  |  |  |
| Rs2 | 51.559 | 51.217 | 51.559 | 51.835 |
| f2 | 39.410 |  |  |  |
| Ri2 | 167.241 | 170.942 | 167.241 | 164.410 |
| Waist at mirror 2, wM2 | (dia. = 40) | 8.457 | 8.363 | 8.291 |
| (2 | 50.0( |  |  |  |
| zw(Cass.) | 150.00 | 149.482 | 149.435 | 149.399 |
| wCass. |  | 2.996 | 2.729 | 2.505 |
| dmirror-subrefl |  | 6148.95 | 6148.99 | 6149.03 |
| wsubrefl | (dia. = 750) | 317.407 | 317.409 | 317.410 |
| Rsubrefl | 6000.00 | 6000.000 | 6000.000 | 6000.000 |
| Edge Taper (dB) | 12.00 | 12.12 | 12.12 | 12.12 |

Dimensions in mm.

Table 14 Band 9 parameters

### ALMA band 9 optical layout

### Abstract/Introduction

In this report a mm wave optics prototype for an Atacama Large Millimeter Array (ALMA) receiver cartridge is discussed. Mainly the ALMA frequency band 9 (602-720 GHz) is considered. However the same design approach is applicable to the receiver optics of any other ALMA bands.

The high frequency cartridges (bands 7-10) have been decided to have no intermediate optics between the telescope secondary mirror and the cartridge cold optics. (See notes of Tucson optics meeting). Consequently, in the optical design of band 9 cartridge full signal path with all focusing elements are considered as free design parameters.

In this report a concept of choosing and optimizing these parameters is discussed. The design starts from an optimal corrugated and diagonal horn field representation. A possibility of distortion compensation by a pair of ellipsoidal mirrors is discussed. A concept of frequency independent radiation coupling between the horn and the Cassegrain telescope system is presented. An expression for parameters of two elliptical mirrors giving rise to frequency independent matching of the horn to the telescope is given.

A practical corrugated horn for signal path of mixer and a practical diagonal horn for local oscillator (LO) part of mixer are proposed. Based on the horn and the ALMA prototype antenna design a two-mirror layout for ALMA band 9 is proposed.

The alignment accuracy of optical components within the cartridge is considered. The alignment accuracy between the cartridge and the secondary mirror is also considered.

### Design concept

In this part a few theoretical facts, used in the following practical design, are discussed.

###### Corrugated and diagonal horn representation

The essential part of the quasi-optical design is the feeds. The corrugated horn has been shown to have a very good Gaussian beam over at least 1.5:1 frequency range. The possibility of machining of these horns has been shown for frequencies at least up to 1 THz. The coupling efficiency to the zero order Gaussian beam can exceed 98 % for this type of horn. That is why we will use it as feed in the signal path of band 9.

Throughout this report we will be using the following expression for the electrical field distribution over the horn aperture:

,			(1)

where  is radius over the horn aperture, is the radius of horn aperture and is the horn slant length. We do not consider the cross polarization in this representation, so the formula is given for main polarization. Expression (1) is slightly different from the one given in [1]. It was modified for normalization purpose such as the beam coupling given by:

.						(2)

is equal to 1 when . The coupling between the horn and the fundamental Gaussian beam is then simply given by (2) where Gaussian beam distribution is used for  and is used for . In this design we will use the fact that the radius of curvature of the beam in the horn aperture is very close to horn slant length. It can be found that Gaussian beam radius at the corrugated horn aperture should be  (for aperture illumination taper 8.6 dB). Given this condition the optimum Gaussian beam will have a waist size and distance from horn aperture (towards horn apex)are given in following expressions:

,						(3)

. 						(4)

More than 99% of power in the Gaussian beam with parameters given in (3) and (4) is coupled into the corrugated horn. For the geometrical optics limit ( in (4)) we find that geometrical optics image is located in the horn apex. This fact will be used for building an optical system for band 9 using geometrical optics.

### Equivalent diagonal horn

The band 9 mixers will use a quasi-optical LO injection. We propose to use the diagonal horn as a feed for the LO source. There are several reasons for this choice: the antenna beam pattern of such a horn is reasonably good, the optimum Gaussian beam coupling for this type of horn can be as high as 84 % and – quite important – a diagonal horn is much easier to produce than a corrugated horn. The overall coupling between optimum corrugated horn and optimum diagonal horn will be about 82 % that is enough to efficiently couple LO signal in a mixer.

The electrical field in the aperture plane of a diagonal horn is described by following equations:

,	(5)

,	(6)

; ,						(7)

where is the co-polar component (along axis v), is the cross-polar component, is aperture size, is horn slant length, and ,are orts of coordinate system as shown in Figure .

Figure 49: Diagonal horn geometry.

An optimum Gaussian beam coupling of ~ 84 % to this type of horn is achieved when the fundamental mode beam radius . The beam radius of curvature in this case is also equal to . The waist position and size can be defined by the same set of equations (3) and (4).

As it will be shown in sections Error! Reference source not found., 0 it is especially advantageous if corrugated and diagonal horns to match has the same optimal fundamental mode beam waist sizes and positions. This can be achieved if the diagonal horn size is related to the corrugated horn radius as  and slant lengths of both radiators are equal. This symmetry allows to achieve frequency independent coupling and to avoid beam distortions when using two identical elliptical mirrors to couple one horn to another.

.

### Frequency independent coupling between horn and telescope beam

The optical train layout is shown in Error! Reference source not found.. This is analogous to the layout shown in Error! Reference source not found.. Two elliptical mirrors M1, M2 are used to match the beam from a telescope secondary mirror to a horn. We will discuss here the choice of mirror parameters (R1, R2, R3 and R4) for providing frequency independent coupling between telescope and mixer.

As it was discussed in section 0 the optimal fundamental Gaussian mode beam should have the radius of curvature equal to horn slant and at the same time it must have beam radius  where  is horn radius. In order to achieve that we use the known properties of an optical system. If the system is arranged in such a way, that it reimages the pupil (in our case the secondary mirror) onto the horn aperture with the required beam size and, at the same time, it reimages the focal point into the horn apex then beam radius of curvature and beam radius are independent on frequency. That allows to use geometrical optics relations to calculate main parameters of the system.

Above conditions can be satisfied by system of three mirrors. Two mirrors can determine the magnification of the system and the third mirror can be used as a field mirror, specifying the pupil image position at the aperture of the horn. However, for specific set of parameters field mirror is not necessary.

It can be shown, that based on two free parameters , the other parameters of system can be calculated using following expressions:

(8)

where  is the system angle magnification, is the horn length,  are mirror focal distances. All other parameters are clear from Error! Reference source not found..

The beam radius at the horn aperture  can be adjusted to realize different edge illumination of telescope secondary mirror. The following expression can be to calculate from edge taper (dB) and horn radius :

.						(9)

A fundamental mode Gaussian beam propagation trough the system calculated by using (8) is shown in Figure . Gaussian beams are shown for  and beam radii, input and output distances (, ) Mirrors should pass diameter beam in order to reduce truncation losses. The calculation was done for lowest band frequency 600 GHz assuming that mm,  mm and the horn.

The output waist position and size of this two-mirror system can be calculated using standard Gaussian optics formulae. As soon as a dependence of output beam waist position and size from frequency is known, equations (2), (3), (4) can be used to calculate final coupling between telescope and horn. Result of such calculation is presented in Figure  by solid line. The coupling appears to be frequency independent. The coupling for an equivalent Gaussian beam telescope system is shown in the same picture by the dashed line. It appears to be frequency dependent.

Figure 50: Optical train for a practical system. Gaussian beam contours for and radius are indicated as well as geometrical optics beam. Calculations were made for frequency 600 GHz and edge taper of 12 dB.

Figure 51: Optimized (solid line) and Gaussian beam telescope (dashed line) coupling between fundamental Gaussian mode beam illuminating the telescope secondary at 12 dB edge taper and a corrugated horn through two-mirror optical system.

### Proposed layout

3.2	Design requirements and concept

The band 9 receiver optics has the following main design goals: a) all optics is mounted in the cartridge structure shown in fig. 2; b) the LO power source is located on the 90 K stage of the cartridge; c) most of the optics is located at 4 K level since SIS mixer technology is used; d) two orthogonal linear polarizations should be received from the sky; e) the secondary mirror edge illumination taper should be 12 dB and should not depend on frequency within ALMA band 9.; f) design should be based on the reflective optics elements and five waists size beam should be put through; g) Cross polarization signal level should be less than –20 dB from the power in the main polarization.

ALMA antenna is a classical Cassegrain system. The primary mirror diameter is about 12 m, secondary mirror diameter is 0.75 m, and the distance from antenna secondary mirror to focus is 6 m. Antenna beam towards receiver is #f8 angular size. This is an input beam for band 9 receiver. The receiver position is 0.1 m offset from main symmetry axis of antenna.

Additional attention should be paid to the small series production of the optics. ALMA project requires 64 receivers to be built. Because of this requirement it was decided to build all the optics using conventional CNC machining and make machining tolerances sufficiently tight to skip the additional alignment procedure by a laser beam.

Since the frequency with band 9 is much lower than that of optical light only 7 micron RMS mirror roughness is required, and the tightest tolerance for this particular design is about 40 microns. These parameters are well within reach of conventional CNC machining techniques. Note that 7 micron RMS will not allow the optical checks for mirror alignment and therefore use of an submm wave antenna beam pattern measurement system is essential to asses the quality of optical system. In order to verify the design concept of using direct CNC machining for these frequencies, a simple model for a signal chain – a two-mirror block has been built, together with a mixer horn, the details of it will be presented later in the section about measurement results.

Drawing of signal path is presented in fig. 3.1. Telescope focus is located in the point FP. Two elliptical mirrors (M3, M4) are used to reimage the secondary mirror of telescope (M2) into the mouth of a mixer horn with the size, that is appropriate for 12 dB edge taper. The quarterly focal point (the second focal point of mirror M4) coincides with an apex of the corrugated horn H1.  This construction allows for frequency independent coupling of the telescope beam to a corrugated horn feed. Mirror diameters are chosen to put through a 5 w size beam.

Fig. 52: Layout of optics. Beam dumps and one of the signal polarizations are not shown.

The second polarization beam is split off from the main beam at 90 degrees angle by means of a grid G1. The grid is located between mirrors M3 and M4 at the narrowest point of the beam (near tertiary focus).  M3 is used for both polarizations and an additional mirrors M4’, M5’, and M6’ are used for forming an orthogonal polarization beam arriving at second mixer horn H2. The cross polarization signals are absorbed by a special absorber plate mounted behind the grid G1 at 4K level.

2.3	LO insertion

Local oscillator signal is inserted quasioptically using a beamsplitter B1 in fig. 3.1 It is mounted between signal horn and mirror M4. A 12 micron Mylar film is used as beamsplitter material that corresponds to approximately 7% of LO signal insertion. The LO signal is then reflected towards 90 K plate of the cartridge where additional mirror M6 and final local oscillator multiplier (quintupler) is located. The quintupler beam is formed by a horn H2. The system is designed to put through a  four waists size beam. Additional infrared heat filters are mounted on 12 K stage to decouple 4K and 90 K levels thermally.

The second polarization has its LO inserted in exactly the same way using mirrors M5’ and M6’ that are identical to M5 and M6 respectively. It has its own multiplier and horn H2’. This polarization is not shown in fig.  3.1

An absorber plate is mounted behind each of beamsplitters for both polarizations to dump LO power that is not coupled into the beam.

The full unfolded band 9 optics layout schematic is presented in fig 3.2.

Fig 53. Band 9 optics layout schematic.

### Signal path details

The signal path is symmetrical for both vertical polarization (VP) and horizontal polarization (HP). For HP the path is as follows: a telescope focal point (FP in fig. 1) followed by mirror M3, grid, mirror M4, beam splitter for LO insertion and finally by the mixer horn U1. For VP the signal follow from FP to the same mirror M3 then, reflected by the grid, comes to mirror M4’, beam splitter, and mixer horn U1’.

The FP coincides with one of the focal points of the mirror M3 . The second focal point of mirror M3 coincides with first focal point of mirrors M4, M4’. The grid is placed in this point. The second focal point of ellipses of mirrors M4, M4’ coincides with apexes of horns U1, U1’, respectively. Mirrors M4, M2’ as well as horns U1,U1’ are identical.

Here is the table of all relevant distances for signal path:

| Distance indicator (fig. 3) | Distance (mm) | Comment |
| --- | --- | --- |
| D1* | 150 | Distance from FP to mirror M3 |
| D2* | 53.453 | Distance from foci of M3, M4, M4’ (point F1) to M3 |
| D3* | 42.453 | Distance from foci of M3, M4, M4’ (point F1) to M4’, M4 |
| D4* | 60 | Distance from horn U1, U1’ apex to mirror M4, M4’ |
| D5* | 50** | Distance |
| Grid reflection angle projection | 125**(deg) | Angle between of HP and VP beam paths after passing the grid, projected on horizontal plane (X-Y) |

* All distances are measured along the beam path

** Free parameter (can be changed by designer)

The mirror description table:

| Mirror | a (mm) | b (mm) | e (mm) | f (mm) | Diameter | Bending angle 2( (deg) |
| --- | --- | --- | --- | --- | --- | --- |
| M3 | 101.727 | 80.8407 | 0.607022 | 39.4096 | 45 | 50+0.94 |
| M4, M4’ | 51.2266 | 45.7411 | 0.450222 | 24.862 | 40 | 50 |

* Input beam comes in 0.96 deg off vertical direction, output beam of M3 comes 50 deg off vertical direction. See fig 4.1

table 15

Fig 54: Sketch of a signal path for horizontal polarization.

The corrugated horn description table:

| Horn | Horn length (mm) | Aperture diameter (mm) |
| --- | --- | --- |
| U1, U1’ | 15.4407 | 5.0628 |

The goal telescope illumination taper calculated using fundamental Gaussian mode beam is 12 dB. Optics is designed to put 5Waist beam diameter through.

### LO path details

LO path is also the same for VP and HP. I will describe only VP LO path. It starts with mixer horn U1 apex than a Mylar beam splitter (12 micron currently) will follow. The beam splitter is rotated around direction of incoming E-vector by 45 degrees making the beam deflected by 90 degrees. Then beam comes to the mirror M3 and M4 and, finally, arrives into LO source corrugated (diagonal) horn (LO).

The mirrors and horns are joined by coinciding the focal points of appropriate ellipses that form the mirrors (similar to signal path).

Table of relevant distance for LO path:

| Distance indicator (fig. 3) | Distance (mm) | Comment |
| --- | --- | --- |
| a1* | 28 | Distance from apex of horn U1 to beam splitter |
| a2* | 37 | Distance from beam splitter to mirror M5 |
| a3* | 191.09 | Distance from mirror M5 to common focal point F2 |
| a4* | 84.5901 | Distance from mirror M6 to common focal point F2 |
| a5* | 27.6875 | Distance from LO horn to mirror M6 |

* All distances are measured along the beam path

The mirror description table:

| Mirror | a (mm) | b (mm) | e (mm) | f (mm) | Diameter | Bending angle 2( (deg) |
| --- | --- | --- | --- | --- | --- | --- |
| M5, M5’ | 128.045 | 78.8062 | 0.782684 | 48.5019 | 40 | 90 |
| M6, M6’ | 56.1388 | 34.2205 | 0.792732 | 20.8598 | 40 | 90 |

The corrugated horn description table:

| Horn | Horn length (mm) | Aperture diameter (mm) |
| --- | --- | --- |
| LO, LO’ | 7.0433 | 2.4 |

Table 16

LO optics is designed to put 4Waist beam diameter through. The equivalent diagonal horn maybe used instead of LO, LO’ corrugated horns.

Fig 55: 3D drawing of all band 9 optics beams, showing final beam layout, taking into account beam sizes.

Fig. 5.2 shows the drawing of beams in 3D. The signal from the telescope comes for top right. The drawing is shown in scale.

### Mirror alignment tolerances

In this section an individual mirror and horn alignment tolerances are considered. Some mirror offsets can be compensated or by refocusing (shift in the telescope secondary mirror) or by calibrating pointing offsets. Some facts that are stated in [4] were used.

Let us consider the offset of mirror M4 in the optical train while all other elements are kept in the same absolute position. The output waist position can be calculated by using ray matrices of elements. The dependence of optical coupling vs. mirror offset is shown in Figure . The tolerances for 1% of efficiency loss are maximal for highest frequency of 720 GHz and correspond to the range of –1.63 … 1.88 mm.

However, if one allow for a in change the distance between focal plane and first mirror (it can be achieved by adjustment of the telescope secondary mirror) the position tolerances of this mirror offset becomes much less critical: -2.3 … >3 (or even >14) mm. This is illustrated by Figure . The same considerations can be applied to all relative movements making tolerances less critical.

Figure 56: Coupling through the system vs. mirror M4 offset for different frequencies. Solid blue line corresponds to 600 GHz, dashed red line corresponds to 720 GHz, and dotted green line corresponds to 660 GHz.

Figure 57: Optical coupling versus telescope focal plane offset and mirror M2 offset. Distance between contours is 1%. Central white area corresponds to 100%. Additional truncation is not taken into account.

Figure 58: Local coordinate system used for mirror tolerance calculations. X- and z-axes are in the plane of the beams. Z-axis is perpendicular to the mirror surface.

For calculating of the actual alignment tolerances mirror bending angles should be taken in to account. Mirror offset can be described by shifts and rotations in three orthogonal axes as shown in Figure . The chief ray was propagated through the system and output waist offset due to movement of one mirror was calculated in the paraxial limit. Aberrations and distortions are not taken in to account in this calculation as an effect of second order. Results of calculations allowing for 1% of relative loss per degree of freedom are shown in table Table 1. The second column shows mirror/horn displacement when telescope secondary focus position is kept fixed. The third column shows the same tolerance provided that telescope can be defocused and focal plane offset is calibrated out. The fourth and fifth columns show optimized values and offsets. It can be seen that allowing for some adjustments makes some tolerances less strict. Most critical type of movement is therefore mirror rotations.

Table 1 Alignment tolerances budget

| Misalignment type | Offset (non compensated) | Compensated offset | Defocus (mm) | Focal plane offset (mm) |
| --- | --- | --- | --- | --- |
| Mirror offsets |
| Mirror M3 x-axis offset | 0.067 mm | 0.157 mm | 0.366 | -0.528 |
| Mirror M3 y-axis offset | 0.058 mm | 0.136 mm | 0.366 | -0.528 |
| Mirror M3 z-axis offset | 0.185 mm | 0.260 mm | -1.19 | 0.252 |
| Mirror M4 x-axis offset | 0.045 mm | 0.075 mm | 0.352 | 0.331 |
| Mirror M4 y-axis offset | 0.041 mm | 0.068 mm | 0.352 | 0.331 |
| Mirror M4 z-axis offset | 0.423 mm | 0.575 mm | -2.05 | 0.236 |
| Mirror rotations |
| Mirror M3 x-axis rotation | 0.037 ( | 0.088 ( | -0.303 | -0.534 |
| Mirror M3 y-axis rotation | 0.065 ( | 0.153 ( | -0.303 | -0.534 |
| Mirror M3 z-axis rotation | Inf | Inf | -- | -- |
| Mirror M4 x-axis rotation | 0.028 ( | 0.044 ( | -0.31 | 0.3 |
| Mirror M4 y-axis rotation | 0.051 ( | 0.081 ( | -0.31 | 0.3 |
| Mirror M4 z-axis rotation | Inf | Inf | -- | -- |
| Horn offsets |
| Horn lateral offset | 0.093 mm | 0.137 mm | 0.341 | 0.269 |
| Offset along the beam | 1.3 mm | 1.3 mm | 0.512 | 0 |
| Horn rotations |
| Horn tilt | 0.817 ( | 1.11 ( | 0.188 | -0.231 |
| Rotation about beam axis | 5.74 ( | -- | -- | -- |

Table 17

### Optics design verification

In order to verify if a selected machining techniques or design approach works a simplified model of a signal path consisting of two mirrors M3, M4 and mixer horn mount has been built. It is shown in fig. 7.1

Fig.59: A prototype two-mirror block for evaluating production techniques.

A prototype ALMA corrugated horn, suitable for room temperature has been made. It is mounted in the bottom block. The photograph of the two-mirror block arrangement is shown in fig 7.2

Fig 60: Photograph of prototype two-mirror block

Two prototypes have been made by companies WITEC and MECON. These prototypes have been measured by using a alma prototype corrugated horn and following measurement technique.

7.2	Standing waves compensation method

A Measurement System: The measurements were made in the near field of the optics under test and similar to that described in [6].  A small probe, which was the transmitter in front of the receiver in the X, Y and Z planes.  These movements were made in small discrete steps and at each point values of amplitude and phase were taken.  The transmitter was a phase locked Gunn oscillator working between 100-120 GHz, which fed a X6 multiplication chain to have a transmitted signal between 600 and 720GHz. A small part of the Gunn signal was coupled off to act as a reference for the phase.  The signal was received through the optics under test with a harmonic mixer.  A frequency about 20GHz was used from a synthesiser to mix both the reference and received signals so there was an IF of 4GHz and 4/6GHz respectively. The reference channel was multiplied by 6 so that 2 coherent signals of 4 GHz can be fed into a vector voltmeter, which gives the phase and amplitude information.  This system is essentially a homodyne system.

For most of the measurements a network analyzer with an access to internal reference and signal  ports was used. This allows for using very small detection bandwidths up to 10 Hz (30 Hz was used in the measurements).

7.3	Standing waves compensation method

A standing wave in the setup was suppressed by using the following technique. Two data points were taken with lambda over four separation in z-axis. These two points were added up with correction of the phase of Pi over two. The forward signal is than added constructively, unlike the first order reflections, which has a phase difference of Pi. These reflections are added destructively.  This method allows effectively suppress parasitic effects due to first order reflections for beams, close to a parallel. Band 9 receiver f#8 beam is close enough to achieve good standing wave suppression without degrading the quality of measurement itself. Additionally, an absorber plate around the source was used to decrease the level of reflections.

A small approx 2 x 1 mm flared waveguide probe was used as a radiation source. Its antenna beam is much wader than receiver f#8. No correction for source beam pattern is needed for analyzing results of measurements.

7.4	Room Temperature detector and saturation

An SLED (super lattice electronic device) was mounted instead of an SIS junction in one of our mixer holder. That allows for using it mechanically with exactly the system which is going to be cooled down. This detector potentially has better conversion efficiency as conventional diode. Although, no specific matching circuit was designed to couple the SLED to an RF environment, signal to noise ratio of 72-80 dB has been obtained for all frequencies in ALMA band 9, using about 50-70 microwatt as an input signal. All measurements were done at room temperature. The SLED was pumped subharmonically. 36th harmonics of LO was typically used.

Since SLED is relatively new detector device for this type of measurements, a special attention was paid for detector saturation by the input signal. To check this effect, a measurements were done for the same beam of corrugated horn and scanning ranges while changing source output power. Results of this measurement are presented in fig. 7.3 and 7.4 for amplitude and phase respectively.  No significant compression was found in the data as well as phase appears to be stable even for very significant drop (-33 dB) of input signal power.

Fig.61: Normalized amplitude field distribution measured at different signal source levels to check for a detector saturation effects. (ALMA corrugated horn)

Fig.62: Normalized phase field distribution measured at different signal source levels to check for detector saturation effects. (ALMA corrugated horn)

### 7.5	Laser beam propogation

The two-mirror block, presented in fig. 7.1 was produced by a CNC machining technique in WITEC. Mirror surfaces were machined by a boll mill in the 5-axis CNC machine. After light polishing, the surface quality was good enough to put through a laser beam. The beam itself can be visualized by applying a water vapour fog during long time exposure of digital camera. The result is shown in fig. 7.5

Fig.63: Laser beam sent through machined two-mirror block.

Intermediate (tertiary focus) and final (quarterly focus) are clearly visible. Some beam splitting can be visible at lower right corner of the picture. This is due to approximation errors that occur during milling of the mirror surface. Note that frequency, at which the effect occurs, is 1000 times higher than the required frequency.

### 7.6	RF beam pattern measurement and analysis

A 2-D plot of amplitude and phase beam distributions are shown in fig.  7.7 and 7.8 respectively. The mirror symmetrical axis coincide with Y-axis of scanner.  One can see that a central maximum has a symmetrical shape both in phase and amplitude. A low levels of sidelobes is observed. A round ring structure at lower levels can be explained by periodical deviations of mirror shape from nominal curve due to machining strokes of the mill tool.

Fig.64: Measured near field beam amplitude distribution of the two-mirror block at -50 mm from the waist plain. Frequency is 672 GHz. (WITEC mirror)

Fig.65:  Measured near field beam phase distribution of the two-mirror block at -50 mm from the waist plain. Frequency is 672 GHz. (WITEC mirror)

Amplitude and phase information allows to calculate an overlap integral of the measured data with fundamental mode Gaussian beam. Ideally, this beam has six parameters, which can be determined from the data by maximizing Gaussian beam coupling: beam waist size, waist position (X,Y,Z), and two beam tilt angles. If the scanning plane is referenced to a mirror surface by a calibration device, obtained parameters allow to conclude if the production errors are still

Fig.66: Normalized amplitude field distribution measured along mirror asymmetrical axis at different signal frequencies.

Fig.67: Normalized phase field distribution measured along mirror asymmetrical axis at different signal frequencies.

Fig.68: Normalized amplitude field distribution measured along mirror symmetrical axis at different signal frequencies.

Fig.69: Normalized phase field distribution measured along mirror asymmetrical axis at different signal frequencies.

acceptable and what the efficiency loss can be. The Gaussisity of the beam shown in fig. 7.7-8 is about 98%, which is very close to an ideal situation. The waist size, offsets and tilt angle are within the required tolerances. It produces less than 1% efficiency loss, compared with an ideal case.

Measured beam cross-sections both for symmetrical (Y) and asymmetrical (X) mirror axes are shown in fig. 7.9-12. These measurements were done for several frequencies in ALMA band 9. Note that beam quality maintains over whole frequency range except the lowest frequency. At the lowest frequency, some deviation can be explained by a corrugated horn beam pattern change. A new horn design is underway.

As expected, the beam is largely symmetrical for symmetrical mirror axes. Visible operations effects are present in the cuts along the asymmetrical mirror axes. These effects, give rise to a beam tilt with respect to a nominal beam direction. Beam tilt, determined from measurements, is still within the required boundaries.

Finally, a far field antenna beam pattern can be determined from the 2-D data of fig. 7.8-9 by means of Fourier transform. The resulting amplitude angular distribution is shown in fig. 7.13 and central part of the distribution is shown in fig. 16 compared with the angular size of ALMA antenna secondary mirror. Since mirror is in the far field zone of the waist, this gives a good indication of the illumination edge taper.  From fig. 7.14 one can conclude that the edge taper is very close to the required 12 dB and illumination pattern of the secondary is well centred. A semi-round fringes are visible at the beam pattern at very low signal levels. These fringes are again due to approximation error of the CNC machine (and due to tool movement stroke direction). However, still visible, these effects do not degrade significantly the illumination pattern at the secondary mirror.

Periodical mirror surface deviations produce a various peaks at far field pattern, see fig. 7.13. The angle of these peaks allows to determine the period of these deviations. Random deviations with white spectrum result in increase of a spill over from the main beam towards all directions uniformly. Good signal to noise level obtained in the figure and low level of peaks due to periodical deviations suggests that the selected production technique is sufficient for application in ALMA band 9 receiver.

Fig.70: Calculated far field amplitude angular distribution of the two-mirror block. Frequency is 672 GHz. The boundary of secondary mirror and central blockage of antenna are presented by a dashed line. (WITEC mirror)

Fig.71: Far field amplitude angular distribution of the two-mirror block calculated from near fireld pattern. Frequency is 672 GHz. (WITEC mirror) Zoom in from fig 7.13

7.7	WITEC vs MECON mirror system

Measurements of two mirror block prototype made by company were also performed in the same system. The far field pattern for MECON block is shown in fig 7.15. This picture should be compared with fig. 7.14  of the same measurements for MECON mirror block. Much more pronounced structure is visible off the main beam for MECON mirror block. The poorer quality of this mirror can also be seen by the visual inspection. A several maxima off beam are produced by a periodical deviation of mirror surface from a nominal one. However, if the amplitude of this off main beam peaks is considered, the MECON mirror would be quite acceptable as well. The illumination of the secondary in fig 7.15 is slightly off center, due to aberrations effect. One can also see, that secondary mirror edge taper (-9-10dB) is father from a desired value of (-12 dB) than one for WITEC mirror, fig 7.14. These two effects can only be caused by an inaccuracy of mirror positioning.

Fig 72 Far field antenna beam pattern of MECON mirror block. The whole available range is on top, the zoom out to the centre is at the bottom. Frequency is 672 GHz.

7.8	WITEC vs MECON mirror system

A direct comparison of system with LO beamsplitter (Mylar 12 micron thickness) and without was made. The two mirror system was measured consecutively with and without LO beamsplitter. Results of this measurements are presented in fig. 7.16. Virtually no difference can be observed. A small tilt of the ouput beam can be detected by fitting measured patterns to a Gaussian beam. This tilt is well within 1% loss tolerance budget.

Fig. 73 Far field antenna beam pattern measured for two mirror block at 654 GHz. Top picture is measured without beam splitter inserted, bottom picture is measured with beam splitter inserted.

### Conclusions

- Proposed layout is frequency independent

- It is possible to compensate for cross-polar and distortion losses in two (in more than two mirrors) and attempt is made to implement this into this layout

- Alignment tolerances must be considered together with possibility of pointing offset and refocusing of the telescope.

- Proposed layout is physically smaller than Gaussian beam telescope

- Verification of the layout by producing a prototype of a signal optics and making phase and amplitude measurements proved to be successful. Main parameters of the design are confirmed by a direct measurements.

REFERENCES

[1]	 P. Goldsmith, “Quasioptical Systems”

[2]	J. A. Murphy, “Distortion of a simple Gaussian beam on reflection from off-axis ellipsoid mirrors,” Int. J. Infrared and Millimeter Waves, vol. 8, no. 9, pp. 1165–87, 1988.

[3]	H. van de Stadt, private communications

[4]	B. Lazareff , “ALMA Optical tolerances report I and II”

# Band 10

This design will follow the design of that given for Band 8.

Table 18

Figure 74: ALMA band 10 optics

### Optics calculations

Physical optics Appendix H

### Optics measurements

TBD

# Receiver Focus

The telescope focus for the different frequency bands were to be at the point Z = 0, which is the machined top surface of the cryostat top plate.  This was obviously not possible to follow considering the diversity of the different receiver designs with respect to frequency.  The different focal point with respect to frequency can be seen in the graph in figure 49.  The red line shows the different focal points for each band.  The black line shows the focuses for a fixed secondary at the telescope focus and the blue line shows the same for a refoused secondary.  As can be seen all of the bands fit easily into the blue curve, but not into the black.  This is due to the that all of the low frequency bands 1 to 4, have the focus above the cryostat topplate, due to the use of ambient optics.  However the high frequency channels, bands 5 to 10 have the focal points below the top plate.  The green curve is that shown for the focus moved by 50mm into the cryostat, and as can be seen accept for the bands 3 and 4 the majority now fall close.

Figure 75 Telescope focus

# Windows

The role of a cryostat window is fairly obvious, it must act as a good vacuum seal and a the same time let pass the signal frequency band with a minimal signal loss. An added complication to this is that heterodyne receivers require a low coefficient of reflection, which will cover the large band width of the ALMA frequency bands.  Different receiver engineers over the years have used a large variety of ideas for windows, which have been used for different astronomical projects.  The cryostat specification for the vacuum is severely strict.  This has meant that thin plastic windows made from materials like Mylar were not possible. This  final selection was narrowed down to different type of windows,  matched quartz windows, figure 32 and matched HDPE windows figure 33.  The quartz windows use Z-cut quartz as the window, which is a very low loss microwave material, and if thick enough acts as a perfect vacuum window.  However there are 3 main problems with this material:

- A relatively high dielectric constant, which makes matching difficult over a large frequency bandwidth. To do this layers of progressively lower dielectric material are used at a matched thickness.  For most of the ALMA frequency bands 5 layer windows were required.ref.2.

- Quartz is brittle and easily broken, special care is required to avoid damage, which could result in catastrophic effects.  The fact that there is a matching layer would only hide the signs of telltale cracks.

- Matched quartz windows are relatively expensive.  Although large orders can reduce the cost they still have to be hand built.

Figure 76: Matched quartz windows

Figure 77:F.T.S measurements of ALMA band 6 windows

The HDPE (high density polyethylene) is a plastic that has a low loss at millimetric and sub-millimetric frequencies, as a long with PTFE (polytetraflouroethylene) can make ideal plastic windows and filters.  The reason that HDPE was chosen over PTFE was that PTFE has a tendency to creep under the pressure of a vacuum.  To match a plastic like these the usual method to use is to cut grooves in the surface.  There are 2 types of grooves that can be used:

- Rectangular grooves that are a quarter wavelength deep, and usually circular across the face of the window.  These types of grooves were not used since the ALMA frequency bands have a large percentage bandwidth, and they would not work over the whole band.

- Triangular grooves, which are greater than a third of a wavelength at the lowest frequency in the band.  The groove spacing has to be less than ( to have no problems due to diffraction.

- These grooves have little effect on the cross polar as long as the grooves are aligned parallel or perpendicular to the E-field.

The main problem with these windows is that HDPE is a plastic so there is molecular migration through the plastic, which means that the windows need to be relatively thick to reach the tight specifications set by the ‘Cryogenic Group” on the cryostat vacuum integrity.  These windows will be 2 to 3times less in price than the quartz windows, if conventional machining of the grooves is used.  The final HDPE windows were moulded.  The quality of the windows has improved and the price reduced.  The triangular on each side of the cryostat were made perpendicular to each other to cancel any polarization effects that could exist.  B.Lazareff organized the work to mould the windows and filters.

Figure 78: Matched HDPE window

Two types of tests were used on the windows:

- Microwave loss, which is summarised in the table below as the effective increase in temperature of the receiver when a window was put in front of the receiver.  As can be seen 2 types of quartz windows were used.

| Window type | HDPE | QMC | NRAO |
| --- | --- | --- | --- |
| Vacuum | 7x10-7 | 1x10-8 | 1x10-8 |
| Temp. increase B3 | 1K | 2K |  |
| B6 | 2K | 2.5K | 3K |
| B7 | 2K | 3K | 5K |
| B9 | 14K | 4K | 6K |

Table 19: Receiver noise increase with different types of window

The test was a vacuum test on the prototype ALMA cryostat that showed as thought that the use of all plastic windows would give too low a vacuum quality.  Shown in table 8 below are the recommended windows for the ALMA cryostat.  From bands 1 to 4 we would use HDPE windows, 2 of these being lenses, and from Bands 7 to 10 quartz windows would be a used.  For these frequencies there is a lower microwave loss for each of the chosen types of windows.  Bands 5 and 6, which have a relatively large area and would also need a relatively thin window to have a low loss, the only gain that could be attained with plastic windows is cost.  It is suggested that the choice for these 2 bands would be done on a vacuum basis only, and therefore either window could be used.

| Frequency band | Position | Diameter | Window type |
| --- | --- | --- | --- |
| Band 1 | -180.3,180.3 |  | HDPE lens |
| Band 2 | -180.3,-180.3 | 92 | HDPE Lens |
| Band 3 | 54,-306 | 66 | HDPE Window |
| Band 4 | 54,306 |  | H DPE window |
| Band 5 | 173.2,-173.2 |  | Quartz |
| Band 6 | 173.2,173.2 |  | Quartz |
| Band 7 | 100,0 |  | Quartz |
| Band 8 | 0,-103.3 |  | Quartz |
| Band 9 | 0,100 |  | Quartz |
| Band 10 | -100,0 |  | Quartz |

Table 20 ALMA window selection

Table 16

# Filters

D.John and S.Navarro at IRAM Grenada in Spain carried out most of the filter work.  They had a lot of help from C.Cunningham at HIA for the FFT measurements and from A.Barychev at SRON for the sub-millimeter measurements.  A-L.Fontana, F.Mattiocco and B.Lazareff continued these measurements.  The filters are used to keep incident the infrared radiation from warming the cryostat and at the same time having a small loss on the relevant frequency bands.  The ALMA cryostat has 2 screens to fit these filters, the 90K and the 15K.  It was initially thought, that it would only be necessary to put filters on the 90K shield, where PTFE acts as a very good infrared filter.  The filter construction would be as shown below.  There would be a solid PTFE disk, which would be matched in the same way as the windows above, that are thermally fixed to the 90K shield.  The solid filters as with the windows need to be matched across the frequency bands.  The same matching technique of triangular grooves is used.  In the test cryostat PTFE was used, but for the production cryostats PFA(Tetraflouroethylene-perflouro(alkoxy vinyl ether)) replaces PTFE.  This material is mouldable Teflon, and so moulding techniques can make the filters.  The RF properties were measured by F.Mattiocco using a cavity resonator at ~240GHz and are shown in the table below.  Above the solid would be a floating filter for bands 5 and 6, which is a thin PTFE foam layer of Goretex, Mupor or Zitex, that is attached mechanically, but not thermally to the 90K shield.   Each of the floating filters would cut the incident infrared energy by about 50%, ALMA memo 269 Clarke and D’addario.  For the sub-millimeter bands 8,9 and 10 a series of floating filters are used.

Figure 79: 90K filter construction

Calculations and measurements indicated that the filters in table 10 below would be efficient enough to allow suitable cold measurements at the 4K stage.  However measurements on the ALMA prototype showed that the 90K shield was at 140K, which meant that these filters were not working effectively and added filters were required at the 15K shield.  The filters used were 1mm thick Mupor, which is a PTFE foam material.  The thickness and the choice of the material will have to be altered for the different frequency bands.  If the cryogenic group can lower the temperature of the 90K shield, it might be possible to remove these filters especially for the sub-millimeter bands.  The filters with the frequency bands are given in table 9.

| Dielectrics | F GHz | Q0 | Qext | QL0 | QLD | ε R | tan δ | T mm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HDPE 1999 | 240.16 | 164400 | 2.4 10 6 | 153860 | 38530 | 2.309 | 2.9 10 -4 | 9.86 |
| HDPE 2001 | 242.21 | 164373 | 2.4 10 6 | 153860 | 42249 | 2.310 | 2.5 10 -4 | 9.765 |
| HDPE 2003 | 245.75 | 175148 | 2.4 10 6 | 163946 | 38298 | 2.299 | 3.5 10 -4 | 8.02 |
| PFA | 241.169 | 188600 | 2.7610 6 | 176518 | 26878 | 2.049 | 4.6 10 -4 | 10.00 |
| TEFLON | 245.325 | 183781 | 2.7 10 6 | 172027 | 31844 | 2.037 | 6.2 10 -4 | 5.98 |
| REXOLITE | 232.422 | 216490 | 3.2 10 6 | 202644 | 30000 | 2.532 | 20 10 -4 | 2.02 |

Table 15: RF properties of different plastics

Table 30 Infrared filters

# The Optics Calculations

A series of optics Gaussian and physical optics calculations were made at the Cavendish Laboratories by C-Y.Tham, with the help of S. Withington.  For band F.Tercero and J-A assisted 3 them. Fernandez Lopez of the Yebes Observatory.  These calculations and findings are too detailed to put into the main body of the text and are put in as appendices at the end of this report.

All of the bands with the exception of bands 1,2 and 5 have been calculated. Below in figure 53 can be seen.  These reports can be seen in appendices D, E, F, and G.

Figure 81: Real corrugated horn antenna pattern on beam axis coordinates

Full line – E-plane (( = 0), dashed – H-plane (( = 90) co- and cross-polar.

# The Optics measurements

To test the validity of the design of the optics for all of the cartridges a series of microwave measurements have been made.  These measurements have consisted of the following:

- The mismatch and polar diagram measurements for band 1,2,3, (4 horn now changed), 6,7 and 9(polar diagram only).

- The measurement of the cartridge and its optics for bands 3,6,7 and 9(2 mirror only).

These measurements were compared with the theory, supplied by the theoretical study and design of the optics.  With respect to the horns this has meant an iterative modifications for the designs for the bands 3,4,6,7 and 9, where the measurements have shown that the mismatch or the polar diagram have not agreed satisfactorily with the theory.

The measurements on the systems have shown that the design does follow theory with respect to the specification of the tolerances.  These measurements have been summerised in the receiver band chapters.

# Common Optics

The common optics has become to be known as the optics above the cryostat in the ‘widget space’.  The actual common optics can be seen in figure 85, which are the 2 lenses for bands 1 and 2, and the mirror assembly for bands 3 and 4.  These will be attached to the top of the cryostat.  The height of the mirrors above the cryostat is 200mm.

The optics in the widget space has to incorporate the optics for the ALMA receivers, the water vapour radiometer optics, quartewave plate the solar filter and the calibration unit.

Fig82: Common optics side view (y-direction)

Figure 83: Common optics Front view (x-direction)

Figure84: Cabin optic layout

Figure 84, 85, and 86 show the proposed optics in the widget space.  Attached to the cryostat will be the ambient optics for bands 1 through 4.  The maximum height of this will be 200mm above the cryostat.  Also fixed to the cryostat will be the WVR (water vapour radiometer) pick off mirror.  This will be a flat mirror fixed to the center of the cryostat and will reflect the beam back up in the direction X = 0, Y positive at an angle of 30 to 40 degrees.  The beam will be incident on an active mirror at a position of X = 0, Y = 550 and Z = + ~300. The beam will now be focused and reflected vertically down to the WVR, which is situated below the FESS (front-end support structure).

### Quarter wave Plate

The quarter wave plate, which will change the band 7 beam from linear to circular polarization, will be a HDPE plate with triangular grooves machined into both faces.  These grooves will be set at 45º to the E vector.  The plate can be put in front of the band 7 window by means of a linear motor attached to the top plate of the cryostat in the X plane at Y = 0.

Figure 85: phase variation of a TPX quarter wave plate

Figure 86: Design of 350GHz TPX quarter wave plate

A design of a triangular grooved quarter wave plate in TPX (polymethylpentene, ε =2.127, tan δ = ~ 5x 10-4) is shown in figure 89 and it’s experimental results in figure 88.  As can be seen for a +/- 1% phase error a band of about 1.7% is possible with this design.

### Amplitude Calibrator

The amplitude calibration unit has not yet been designed.  However it consists of motorized tables that can put a calibration device in front of any of the 10 frequency band windows.  The type of calibration that is required has been discussed by the calibration group and can be summerised in reference 6.  The calibration system will probably consist of a device that requires 4 to 6 separate measurements, which will consist of Sky measurement Tambient, Thot and by the use of a semi- transparent vane Sky + Tambient and Sky + Thot.

For the calibration of bands 1 and 2 due to the size of the beam and that they are HEMT receivers, and therefore not susceptible to receiver saturation another 2-position calibration system could be used.  This is sky and Tambient.  The ambient load could be a foam absorber that rotated into place.

### Solar Filter

At the time of writing this report there has been no work done on this subject.

# Receiver Alignment

As can be seen in the tolerance section in chapter 3, there are 2 forms of error:

- The error that exists within the cryostat.  This could be either in the cartridge or with the cartridge and the common optics.

- The error that exists aligning the cryostat on to the telescope.

Figure 85: Cabin alignment system

The former has been covered earlier in this report.  For the second, the system that is being used is as follows.  The cryostat is fixed in three point at 120º intervals starting at –500,0.  These fixations as can be see are M16 conical bolts, which are fixed into the 1mm thick invar FESS.  The use of conical bolts help with the alignment of the cryostat in the X, Y, and axial rotation planes.  However with respect to the cryostat rotation perpendicular to the telescope axis, the alignment will be made against the FESS at the integration centers.  Shimming the triangular supports on the sides of the cryostat can do this.

# Conclusion

The receiver optics for the ALMA telescopes has been designed.  This has fit into the novel cartridge design of the ALMA cryostat.  The first 4 bands 3,6,7 and 9 have had a complete physical optics design with a optics measurements to support them.  These designs have been shown to be correct across the frequency ranges.  For the bands 4,8 and 10 the physical optics deign has been completed and the manufacture of the components is advanced enough that measurements could be made in the near future.  The horns for bands 1 and 2 have been designed and tested, but await system calculations and measurements.

The tolerances for most of the bands are shown in order to achieve less than a 1% loss across the sub-reflector.

The choice of the windows and filters are given with their dimensions.  These are followed by some of the measurements made to make these choices.

Finally the management of the ‘Widget Space’ is described.

FEND-40.00.00.00.00-16

Band 1 horn design and tests

Quasi-optical analysis of bands 1-10

Physical optics analysis of bands 6,7 and 9

Analysis of ALMA band 3 horn – lens

Physical optics analysis of bands 4,8 and 10

Band 3 physical optics analysis

Reference 1 J.Lamb et al. ALMA memo 362

Reference 2 D.Koller et al ALMA memo 377

Reference 3 S.Guilloteau, A.Bacmann ALMA memo 461

# Text boxes

Chamfer: 0.4

2.54

2.54

M3

M4